## Slide 1: Control Software Summary

## Slide 2: Overview
Pilot Interface
  Overview
  Interface Overview
  Primary Flight Display
  Hand Controls
Mission Control
  Common Operating Picture
  System Status
  Sensor Control

## Slide 3: Pilot Interface Overview
Pilot interface executed from laptop
Controls all vehicle functions, including payloads
Primary pilot controls via COTS controller

## Slide 4: Interface Overview
Map Display
Primary Flight Display
FMV / Imagery Display
Message Center
Health Monitor
Cautions and Warnings

## Slide 5: Primary Flight Display
Airspeed
Altitude
Heading
Roll Angle
Pitch Angle
Yaw Angle
Lateral Speed
Vertical Speed

## Slide 6: Hand Controls
Menu Control Buttons
Select
Back
Shoulder: Increase Altitude
Trigger: Yaw Right or Take Picture
Shoulder: Decrease Altitude
Trigger: Yaw Left
Lateral Velocity Controls
Roll / Pitch Angle Control
FMV Pan / Tilt (when FMV control is active)
FMV Zoom Out
FMV Zoom In
Open/Close Menu

## Slide 7: Common Operating Picture
Integrated map display and route planner
Map
  Weather data
  Threat data
  Blue Force data
  Available data will depend on external connections or organic sensors
Route Planner enables creation / management of autopilot routes
  Can be externally built or locally built
  Intuitive interface
    Right click to add waypoint on cursor
    Select a waypoint to edit

## Slide 8: System Status Page
Health status shows the status of all system components
  Each component can be turned on or off
  Some can be reset or commanded to execute built-in-test
Page can also be used to adjust communications settings
ENG VOLT | 
 | THREAT
Propulsion |  | 
Motor 1 |  | 
Motor 2 |  | 
Motor 3 |  | Volt wan
Motor 4 |  | 
FMV |  | 
Wide Area |  | 
Pay Comms |  | 
Nav |  | 
SRM |  | 
0.80
0.80
0.80
0.80
Fuel State:
0.76
Time Rem:
22 min
Electrical |  | 
Battery |  | 
Breakers |  | 
Comms |  | 
Network |  | 

## Slide 9: Sensor Controls
FMV
  Controlled via primary controller
  Simply push in Button 3 to enable control, then right stick pans and tilts camera
  Zoom is executed via A and B buttons
  The right trigger can be used to take a still image when the FMV control is enabled
Wide Area
  Wide Area images are commanded via the menu
  Pictures can be taken manually or automatically
[Manual] – Automatic – Settings
Press action button to take picture