## Slide 1: Nomad Program Overview

## Slide 2: Overview
Full Motion Video
  Imaging System
  Gimbal
  Data Output
Wide Area Camera
  Cameras
  Control Capability
Communications

## Slide 3: Overview
Full Motion Video Gimbal
Mission Computer
Payload Comm Antenna
Bluefire Wide Area Camera System

## Slide 4: Full Motion Video
Size | 6 in dia
Weight | 9 lbs
Pointing Accuracy | 1.5 deg
Video Format | h.264
Video Metadata | MISB Compliant KLV Metadata
EO | 
GSD (200m Slant Range) | 0.10 m
GSD (1000m Slant Range) | 0.45 m
Frame Rate | 30 fps
MWIR | 
GSD (200m Slant Range) | 0.50 m
GSD (1000m Slant Range) | 0.80 m
Frame Rate | 28 fps
Training Note: This sensor was inspired by CloudCap TASE series sensors, but is completely notional for training.
Separate FMV turrets for either Day or Night capability
Rapid installs (<5 minutes) enable day/night capability
Identical form factor, size, weight and power.

## Slide 5: Bluefire Wide Area Camera
Can operate in either manual or automatic mode
Automatic mode sends images down constantly beneath the vehicle – used for overwatch or survey
User selectable day (electro-optic) or night (low light cameras)
Training Note: Image from Pixia website, not representative of real capability https://www.pixia.com/solutions/hiper-stare/
Weight | 12 lbs
Coverage Area (200 ft AGL) | 380,000 sq ft
Image Format | NITF Compliant JPEG 2000 Compressed
EO | 
GSD | 0.40 m
Latency | 1.8 seconds
Frame Rate | 2 fps
Low Light | 
GSD | 0.60 m
Latency | 2 seconds
Frame Rate | 1.5 fps
4 images are taken simultaneously and sent to the ground station, where they are stitched together into a single image

## Slide 6: Mission Computer and Communications
Hardened Single Board Computer
Runs all mission processing applications
  Health Monitoring
  Product re-transmission
Increased Storage Capability
  Capable of storing 1100 wide area images, or
  95 minutes of video
Sourced from US company
Encrypted at rest
Weight | 1 lb
Processor | Quad Core Intel Processor
Storage | 250 GB Solid State
RAM | 8 GB
Training Note: Image from MPL website, https://www.mpl.ch/t2401.html/
Advanced lightweight tactical datalink
Capable of operating in Ku, L, S and C bands
Data rates up to 40 mb/s
Range up to 15 nautical miles
FIPS 140-2 Complian Encryption
Training Note: Image from L3 Website
https://www2.l3t.com/csw/products/airborne/bandit.htm