## Slide 1: Ground Control Station Overview

## Slide 2: Overview
Overview
Control Interface
Communications
Power System
Tranportability

## Slide 3: Overview
https://www.pelican.com/us/en/product/cases/dji-matrice-600-pro-drone-case/flightline/fltdm600
https://na.panasonic.com/us/computers-tablets-handhelds/computers/laptops/toughbook-31
COTS Rugged Computer
COTS Controller
Control Transit Case
Storage for Computer
Integrated Radios
Additional Processing and Storage
Power Distribution Unit
Vehicle Transit Case

## Slide 4: Control Interface
Control Interface is 100% Commercial-Off-The-Shelf
Panasonic Toughbook + Xbox One
Leverages extensive industry base
Easy replacement
Reduced training
Computer | 
Model | Panasonic Toughbook 31
Size | 13.1 in class
Processor | Intel i7
Storage | 512 Gb Solid State
RAM | 32 GB
Operating System | Red Hat Enterprise Linux
Controller | 
Model | Xbox One Controller

## Slide 5: Communications
Integrated Radios
  UHF Band Control Link
  Ku / L band payload link
Can support multiple antenna options
  Man portable (included in transit case)
  Vehicle mounted (connect through auxiliary cables)
Power Distribution Unit
  Powers all GCS equipment
  Includes battery with 10 hour battery life
  External power connections for 115 VAC and 12 VDC
Additional Processing
  Image processing capability for stitching wide area images
  Auxiliary image/video storage
Control Radio | 
Model | Atlas Inc XR Datalink
Payload Radio | 
Model | Z4 Technologies Multi-band Datalink
Processor | 
Weight | 40 lb (with laptop)
Processor | Quad Core Intel Processor
Storage | 10 TB Solid State
RAM | 32 GB

## Slide 6: Transportability
All Nomad equipment (including vehicle) is transportable in two transit cases
Designed to be unloaded and operational within 10 minutes by a single operator
<100 lb total weight